## Slide 1
DIGNITY
HOLISTIC REHABILITATION
PROVIDE QUALITY OUTDOOR SPACES
PROVIDE BASIC AMENITIES
SENSE OF SAFETY
COMMUNITY
DUE CONSIDERATION TO FUTURE EXPANSION
ADDRESS CLIMATE CHANGE
MIXED USE SPACES
LONGEVITY
SHARED COMMUNAL FACILITIES
COMMON AREAS FOR COMMUNITY ACTIVITIES
MASTERPLAN

## Slide 2
DIGNITY
HOLISTIC REHABILITATION
MAINTAIN THE QUALITY OF SPACES
THERMAL & VISUAL COMFORT
COMMUNITY
DURABILITY OF CONSTRUCTION MATERIALS
CLIMATE RESPONSIVE
FLEXIBLE SPACES
LONGEVITY
INTERACTION WITH THE NEIGHBOURS
COMMON SERVICE CORES
DWELLING UNIT

## Slide 3
150 Dwelling Units (DU)
1 DU /Family
-COURTYARDS
-PLAYGROUND
- WELLS, LOTUS PONDS
-MULTI-PURPOSE COMMUNITY SPACES
-RELIGIOUS SPACES
-CRECHE/PLAYSCHOOL
-GROCERY
-VEGETABLE
-STATIONARY
-PHARMACY
-WATER SUPPLY
-RAINWATER HARVESTING – COLLECTION & STORAGE
-SEWAGE & WASTE DISPOSAL
-ELECTRICITY & RENEWABLE ENERGY
OPEN SPACES
DWELLING UNITS
COMMUNITY SPACES
SERVICES
COMMERCIAL

## Slide 4
CLUSTER LAYOUT
Cluster Footprint–8900 sqft
No. of Dwelling Units - 8
Service Core – 2 Nos.
Green Space - 1173 sq.ft (13%)
GROUND LEVEL

## Slide 5
MASTERPLAN
Community Space
Central Open Spaces
G+2 Units
G+1 Units
Service Core
Connecting Pathways

## Slide 6
MASTERPLAN

## Slide 7
MASTERPLAN

## Slide 8
Option 1 |  | Rapidwall Construction using GFRG units |  | 
Option 2 |  | Conventional Construction using AAC blocks |  | 
Materials and Cost comparison for 2 storey 1500 sqft building |  |  |  | 
Material/Item | Units | Option 1 | Option 2 | Saving in % (Option 1 over Option 2)
Cement | Tons | 16 | 32.55 | 51%
Steel | kg | 1800 | 2779 | 35%
Sand | cum | 20 | 83.37 | 76%
Granite | cum | 38 | 52.46 | 28%
Bricks | units | - | 57200 | -
GFRG Panel | sqft | 500 | - | -
Water | Liter | 50000 | 200000 | 75%
Labour | Mandays | 389 | 1200 | 68%
Construction Time | Days | 21 | 120 | 83%
Wt of Superstructure | Tons | 170 | 490 | 65%
Construction Cost | Lakh Rs | 13.25 | 18.27 | 27%
Source: A seminar Report on affordable mass housing by Suman Pati, 2013 |  |  |  | 

## Slide 9
PASSIVE DESIGN
MINIMIZE SOLAR EXPOSURE (LONGER AXIS IN THE NORTH-SOUTH DIRECTION)
SHADING OF WINDOWS
NATURAL VENTILATION (OPERABLE WINDOWS & PROVISION FOR CROSS-VENTILATION)
USE OF CAVITY WALLS

## Slide 10
WASTE
DISPOSAL
SEGREGATION OF WASTE
FOOD WASTE – COMPOSTING ON SITE
PAPER – (RECYCLE TO HAULER)
E-WASTE (RECYCLE TO HAULER)
RAINWATER HARVESTING
OPTION 1- REED BEDS
OPTION 2 – BIO-DIGESTER
SEWAGE
TREATMENT
UNDERGROUND COLLECTION TANK
PERCOLATION PIT TO BE INSTALLED ON SITE
REDUCE HARDSCAPE AREA
EFFICIENT STORMWATER DRAINAGE DESIGN
WASTE, WATER & ENERGY
RENEWABLE
ENERGY
OPTIMIZE DESIGN TO REDUCE ENERGY CONSUMPTION
UTILIZE ROOFS FOR SOLAR PV’S

## Slide 11
ANURAG BISWAS
ARCHITECT/GREEN BUILDING ANALYST
CHANDRIKA NATH
ARCHITECT
SOURAV BANERJEA
URBAN DESIGNER/ACADEMICIAN
AKSHAY DUA
ARCHITECT
TEAM 1

## Slide 12
ABU TALHA FAROOQI
HEALTHCARE ARCHITECT/ ACADEMICIAN
MOHD. MUSTKEEM
ARCHITECT
SREELAKSHMI HARIDAS
GREEN BUILDING ANALYST/ ARCHITECT
ANKITA RANI
ARCHITECT
TEAM 2

## Slide 13
MEGHA MITTAL
ARCHITECT/GREEN BUILDING CONSULTANT
HARI PRASATH
ARCHITECT/GREEN BUILDING ANALYST
TARUN KUMAR
PURSUING B.ARCH
ANUSHMA MALPANI
ARCHITECT/GREEN BUILDING ANALYST
TEAM 3

## Slide 14: Thank You